University of Arizona SCAFFOLDS Jan 2005 Building/Room:________________________________________________________________ Department:___________________________________________________________________ PI:________________________________________Ext._____________________LabManager:__________________________________Ext._________ Name(s) of Inspector(s):__________________________________________________________Ext.______________ Date:_______________________

|  | Yes | No | N/A | Comments (correction items and responsible person) |
| --- | --- | --- | --- | --- |
| A.MANAGEMENT AND EMMPLOYEE RESPONSIBLITIES& RIGHTS |
| GENERAL REQUIRMENTS |
| 1. Is the scaffold being erected, dismantled and altered under the direction of a competent person? http://www.osha.gov/SLTC/scaffolding/index.html |  |  |  |  |
| 2. Is the footing sound and rigid - not set on soft ground, frozen ground (that could melt), or resting on blocks? http://www.osha.gov/SLTC/pptpresentations/pumpjack_0398/index.html |  |  |  |  |
| 3. Has the erection site been evaluated for hazards such as earth fills, ditches, debris, underground/overhead electric wires, unguarded openings, or conditions created by other trades? http://www.osha.gov/SLTC/video/scaffold/video.html |  |  |  |  |
| 4. Are wheels / castors locked? http://www.jmu.edu/safetyplan/facilmgmt/scaffold/scaffoldsafety.shtml |  |  |  |  |
| 5. Is the scaffold able to hold four times its maximum intended load? |  |  |  |  |
| 6. Are guardrails and toe-boards in place on all open sides? |  |  |  |  |
| 7. Is the platform complete front to back and side to side (fully planked or decked, with no gaps greater than 1 inch)? |  |  |  |  |
| 8. Is the lumber free of cracks, splits, knots, or damage? |  |  |  |  |
| 9. Is the scaffold level? |  |  |  |  |
| 10. Have all components been inspected for defects such as broken welds, corroded members, and missing locks, bent or dented tubes? |  |  |  |  |
| 11. Can the top rail withstand 200 lbs of outward pressure and the mid rail at least 150lbs? |  |  |  |  |
| 12. Are all braces, bearer, and clamps secured all sections pinned or appropriately secured? |  |  |  |  |
| 13. Is there a safe way to get on and off the scaffold, such as a ladder (without climbing on cross braces)? |  |  |  |  |
| 14. Does the scaffold meet electrical safety clearance distances? |  |  |  |  |
| 15. Is the scaffold less than 125 feet in height? |  |  |  |  |
| 16. Is the "X" bracing installed on the ends of the scaffold and every third set of post horizontally and every fourth vertical runner? |  |  |  |  |
| 17. Are severe weather provisions in place i.e. during high winds, rain, snow, or bad weather? |  |  |  |  |
| 18. Have all planks been properly secured to the scaffold structure to prevent them blowing off in the event of high winds? |  |  |  |  |
| 19. Where persons work under scaffold, is a 1/2 inch mesh screen provided between toe-board and guard rail or has the area below the scaffold been cordoned off? |  |  |  |  |
| 20. Are tag lines available for items to be loaded on to scaffold? |  |  |  |  |
| 21. When employees are working on suspended scaffolds, are lifelines firmly anchored to an overhead structure and not to the scaffold? |  |  |  |  |
| 22. Is the scaffold over 10 feet high, (if yes) is personal fall protection available, or are guardrails in place? |  |  |  |  |
| 23. Are guardrails 38-45 inches high? |  |  |  |  |
| 24. Are toe-boards in place and at least 4 inches high? |  |  |  |  |
| 25. Are mid-rails or equivalent in place? “X” on the cross brace must be38” and 48” inches above the platform. |  |  |  |  |
| 26. Does the scaffold have a height to base ratio of at least 4:1? |  |  |  |  |
| 27. Does a competent person inspects scaffold regularly pre shift and once a week? Are the results of inspections recoded in the site log? |  |  |  |  |
| 28. Does the bottom tie to the building placed no higher than 4 times the minimum base width and every 26 feet there after. |  |  |  |  |
| 29. Dose the vertical ties placed at the end of the scaffolds and at no more than 30 feet horizontal intervals. |  |  |  |  |
| 30. Dose the front edge of all platforms more than 14" from the face of the work? http://www.osha.gov/SLTC/scaffolding/scaffold_slides/scaffold_10.html |  |  |  |  |
|  | Yes | No | N/A | Comments |
|  | Yes | No | N/A | Comments |

ADDITIONAL COMMENTS: _______________________________________________________________

________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________