## Slide 1: Slip, Trip and Fall Prevention
Sumith Wijeweera, M.S.
Julia Lerch, Intern
Risk Management Services

## Slide 2: Objectives
Common causes of slips, trips and falls
Measures to take to minimize the potential for slips, trips and falls
Liability
Use of a slip meter to define a slippery/non slippery floor

## Slide 3: Contributing factors
Environment
Social
Physiology
Physiology - balance, hearing, vision
Social – medications, age,
health,
Environmental – flooring
type, maintenance, lighting,
hazards-oil or wet surfaces

## Slide 4: Center of Gravity
Gronqvist, 2001
COM-Center of body mass
BOS-Base of support
COP-Center of foot pressure

## Slide 5: Three Forces
Friction- walking surface and soles of the shoe
Momentum- involves speed and size
Gravity- without support, gravity causes
objects to fall towards the earth

## Slide 6: Slipping
‘a sudden loss of grip, often in the presence of liquid or solid contaminants and resulting in sliding of the foot on a surface due to a lower coefficient of friction than that required for the momentary activity’
Common causes:
-loose mats,
-flooring surface that is worn,
-wet or oily surfaces,
-weather hazards,
-occasional spills,
-insufficient lighting
-aging
Gronqvist, 2001

## Slide 7: Trips
-hit an object, lose your balance and fall
Common Causes:
-Obstructed view
-Poor lighting
-Clutter in your way
-Wrinkled carpet
-Uncovered cables
-Drawers left open
-Uneven walking surfaces

## Slide 8: Falls
-when you lose your balance and descend to the floor
Three types of falls
-same level fall
-lower level fall
-jumps to lower level

## Slide 9: Prevention
Good Housekeeping
Quality of walking surfaces (flooring)
Selection of proper footwear
Appropriate pace of work

## Slide 10: Liability
Proper floor maintenance
Measurement of slipperiness
Limit your risk exposure

## Slide 11: Slip Meter

## Slide 12: American Society of Testing and Materials (ASTM)
Use a slip meter to determine if the floor is safe.
A slippery floor has a reading of below 0.50 Coefficient of Friction (COF).
A non-slippery floor is 0.50 COF or above.
ASTM D 2047 and the Slip and Fall Handbook

## Slide 13: Coefficient of Friction (COF):
-the value between 0 and 1. It describes the degree of interaction between two surfaces.
A higher COF indicates two surfaces in contact have a greater resistance.
A lower COF indicates the two surfaces in contact have less resistance.
ex. Soccer cleats on grass have a greater coefficient of friction than skates on ice.
Wiki.answers.com

## Slide 14: Report Hazards Immediately
If you cannot fix the hazard yourself then:
Immediately report the hazard to your supervisor
Alert or warn others in the area
  Mark the area or stay there until help arrives

## Slide 15
Questions?

## Slide 16: Citations
Grönqvist, R., Chang, W.-R., Courtney, T., Leamon, T., Redfern, M., & Strandberg, L. (October 20, 2001). Measurement of slipperiness: fundamental concepts and definitions. Ergonomics, 44, 13, 1102-1117.
Rosen, S.I. ASTM D 2047 Slip and Fall Handbook. Hanrow Press.
Wiki.answers.com. (2012).